## Slide 1: Secondary Storage – 3.1.8.5
Understand what secondary storage is and be able to explain why it is required
Be able to describe the most common types of secondary storage
Understand how optical media, magnetic media and solid state work.

## Slide 2: Secondary Storage
Computer programs need to be stored in a way that they can be re-loaded when the computer is turned back on.
The user may wish to move programs from computer to computer.
The user may need to back up data/programs as protection against hardware failure, fire or theft.

## Slide 3: Access Speeds (you don’t need to remember these)
LEVEL ACCESS TIME TYPICAL SIZE
Registers "instantaneous" under 1KB
Level 1 Cache 1-3 ns 64KB per core
Level 2 Cache 3-10 ns 256KB per core
Level 3 Cache 10-20 ns 2-20 MB per chip
Main Memory 30-60 ns 4-32 GB per system
SSD < 1,000,000ns 64GB-1TB
Hard Disk 3-10,000,000ns over 1TB

## Slide 4: Secondary Storage types
Hard drive – Traditional mechanical means of storing data
SSD – Faster than HDD, but more expensive
CD / DVD / BluRay – Optical media. Becoming less common.
Tape – Used in large organisations for big back-ups of data.
USB stick – Good for moving data between computers.
Floppy disk – obsolete magnetic storage medium.

## Slide 5: Optical Media – how it works
The tracking mechanism moves the laser into the correct position over the CD;
The CD is spun to ensure all data can be read;
The CD spins slower when the laser/read-head is above the outer tracks;
The laser is shone on to the disk;
The laser is reflected;
Bumps/pits are raised parts of the disk;
Bumps/pits form a spiral from the centre to the outside of the disk;
An opto-electric sensor detects changes in reflectivity;
Bumps/pits and lands represent the two possible bit values

## Slide 6: Magnetic Media – how it works
The platter (circular disk divided into billions of tiny areas) is spun by a motor at high speed. Data is organized in concentric rings called tracks. Each track is broken up into sectors.
Bigger disks can have several platters stacked on top of each other.
The tracking mechanism moves the read-write head into the correct position over the disk platter surface.
The disk is spun to ensure all data can be read.
The read-write head is moved over the desired area of the disk.
The magnetic field (of lack thereof) is read.
Magnetised/demagnetised state represents the two possible bit values.

## Slide 7: SSD – how it works
SSDs use NAND flash memory cells to store non-volatile data. It takes around 10-15ms for a hard drive to locate and read a sector; an SSD can do this in less than 1ms.
Memory cells are grouped together into a page (commonly 4kB in size), and pages are then grouped together into a blocks (usually 128 pages). You write page by page, but can only erase block by block.
Reading from an SSD, the drive controller looks to see whether a voltage is present (0) or not (1) at a specific page.
NAND flash memory can't overwrite existing data like hard drives can. The old data must be erased before new data can be written to the same location. Erasing data is inefficient: When a user deletes data stored on an SSD, no erasing takes place. The operating system marks the information to erase as stale, page by page. The actual erasing only happens when the user wants to write new data to the drive, when Garbage collection takes place. This is the process of moving data in pages for keeping into a new block prior to erasing the block with the material for deletion. Amplification is the effect of having to read and write more data than the user actually wants to store as a result of this process; SSDs become slower to use as they fill up over time.
Writing to an SSD occurs when the controller programs the memory cells to store information. Memory cells store voltage and can be either charged (0) or discharged (1), which allows them to store data in a binary form. Each time a cell is reset, its resistance increases slightly. Eventually, it gets so high the cell becomes unusable, so they can be programed for only a limited amount of time before they become unreliable. This is known as the write-endurance. Wear levelling makes sure that all the drive's memory chips are used, cell by cell, before the first cell can be written on again.

## Slide 8: Practice Questions
2014 5(b). Tablet computers normally use solid state storage media instead of magnetic storage media. State and explain two differences, other than cost and storage capacity, that make solid state media a better choice than magnetic media for tablet computers. [4]
2014 6. Explain how data is read from optical media such as a CD. [5]
Explain how data is read from a hard drive [5]
Explain how data is written to a SSD drive [5]